## Slide 1
Status of RAON heavy ion accelerator facility
M. KWON on behalf of RISP
IBS, Daejeon, Korea
October 12, 2022
Aomori, JAPAN

## Slide 2
001. Project Overview
002. SRF Accelerator Systems
003. Beam Commissioning
004. Summary and Outlook

## Slide 3
Part 1.
Project Overview

## Slide 4: Rare Isotope Science Project (RISP)
Providing high intensity RI beams by ISOL and IF
ISOL: direct fission of 238U by 70 MeV proton
IF: 200 MeV/u 238U (intensity: 8.3 pμA)
Providing high quality neutron-rich beams
e.g., 132Sn with up to 250 MeV/u,
up to 109 particles per second
Providing More exotic RI beam
production by combination of ISOL and IF
Budget: KRW 522.8 billion (US$ 420 million)
for accelerators and experimental apparatus
Period: 2011.12 ~ 2022.12 (1st Phase)
Goal: To build a heavy ion accelerator complex RAON,
for rare isotope science research in Korea.
* RAON - Rare isotope Accelerator complex for ON-line experiments
Construction of research and support facility to ensure the stable operation of the heavy-ion accelerator, experiment systems, and to establish a comfortable research environment
※ Accelerator and experiment buildings, support facility, administrative buildings, and guest house, etc.
Development, installation, and commissioning of the accelerator systems that provides high-energy (200MeV/u) and high-power (400kW) heavy-ion beam
System Installation Project
Facility Construction Project

## Slide 5: RAON Layout
Assembly Bd.
SRF Test Bd.
Waste Storage
Guest House
HQ Office
Electricity Bd.
Control Center
Utility Bd.
Cryogenics Bd.
Low Energy B
Low Energy A
High Energy A
High Energy B
SCL3
SCL2
Accelerator
ISOL
IF
● Conventional Utilities
● Experimental System
● Accelerator System
● RI producing System
Campus Area : 952,066㎡ (including the reservation area of 144,640㎡)
Building Area : 76,259㎡(11 bldgs) with total bldgs. Area of 116,252㎡

## Slide 6: Science Goal of RAON

## Slide 7: RIB production at RAON
Low energy Experiment Hall
High energy Experiment Hall
ECR
ISOL
IF Separator
KoBRA
SCL3
SCL2
 | KoBRA | ISOL | IF Separator
Driver | SCL3(ECR/ISOL) | Cyclotron | SCL3(ECR/ISOL)->SCL2
(Post) Acceleration |  | SCL3 or SCL3->SCL2 | 
Production Mechanism | Direct reactions Multi Nucleon Transfer | P induced U fission | PF, U fission
RIB Energy | < a few tens of MeV/u | > a few of keV/u | < a hundreds of MeV/u

## Slide 8
Part 2.
SRF Accelerator Systems

## Slide 9
SCL31
SCL32
P2DT
SCL21
SCL22
HEBT
IF
KoBRA
QWR
β=0.047
HWR
β=0.12
SSR1
β=0.3
SSR2
β=0.51
SC LINAC 3
18 MeV/u
SC LINAC 2
200 MeV/u
Low-energy
experiments
High-energy
experiments
Transport
Injector
0.5 MeV/u
ECRIS
Cyclotron
LEBT
RFQ
MEBT
Ion sources
ISOL
Simple Diagram of RAON SRF Accelerator
2nd Phase
SC LINAC 1
18 MeV/u
SCL12
SCL11
(in future)
Very low-energy
experiments

## Slide 10
Phased Installation
SCL3 → installation done on 2021 & commissioning on Oct 2022
ECR
ISOL
IF Separator
KoBRA
SCL3
SCL3
High energy Experiment Hall
Low energy
Experiment Hall
Phase 1(~2022)
Injector, SCL3, ISOL beam commissioning
All experimental systems including IF separator system to be installed and machine commissioned
Phase 2(~2029)
High energy Linac, SCL2
SCL3 & Injector
Very Low energy Experiment Hall
SCL2

## Slide 11
MEBT
RFQ
LEBT
SC ECRIS
ECRIS
RAON Injector System
Two ECR-IS on high voltage platforms
14.5 GHz ECR ion source
28 GHz superconducting ECR ion source
LEBT (E = 10 keV/u)
10 keV/u, Dual bending magnet
Chopper & Electrostatic quads, Instrumentation
RFQ (E = 500 keV/u)
81.25 MHz, Transmission Eff. ~98%
CW RF Power 94 kW (SSPA: 150 kW)
MEBT (E = 500 keV/u)
Four RF bunchers (SSPA: 20, 15, 4×2 kW)
Simple quadrupole magnets, Instrumentation
Installation completed and beam commissioning from October, 2020
Ar8+ 10uA @ Beam Viewer(‘21)

## Slide 12
Beam Diagnostic System
LEBT
Wire scanner - 5 sets (4 installed)
Beam Viewer – 3 sets (2 installed)
Bergoz ACCT – 1 set
Faraday Cup – 5 sets (4 installed)
beam Attenuator – 2 sets
2-D Allison Scanner – 2sets (1 installed)
MEBT (Installed)
Wire scanner - 4 sets
Beam Viewer – 1 set
Bergoz ACCT – 2 sets
Faraday Cup – 2 sets
Stripline FFC – 1 set
BPM – 6 sets
Ar8+ 10uA @ Beam Viewer(‘21)

## Slide 13
RFQ and MEBT
PARAMETER | VALUE
Beam Properties: | 
Frequency | 81.250 MHz
Particle | H+1 to U238+33
Input Energy | 10 keV/u
Input Current | 0.4 mA
Input Emittance | 0.012 .cm. mrad
Output Energy | 0.507 MeV/u
Output Emittance | 0.0125 .cm. mrad ~26 keV/u-Degree
Transmission | ~98 %
Duty Factor | 100%
SSPA(60kW*2EA)
[ Ar9+, 2021]
[ Ar8+, 2022]
[ Ar9+, 2022]
[ RFQ transmission (error bar: 3) ]

## Slide 14
1 onsite - 3 VT pits and 3 cavities per pit, 3 HT bunkers
1 offsite (15 Km from site) - 2 VT pits and 2 cavities per pit
Cover all RAON cavities - QWR (82.125 MHz), HWR (162.5 MHz) and SSR1 & 2 (325 MHz)
On-site (Shin-Dong) test facility
SRF Cavity Development

## Slide 15
Frequency (MHz) | Optimum 𝛽 | Eacc (MV/m) | Q0 | # of cavity | # of module
81.25 | 0.047 | 6.1 | 2.4 e+8 | 22 | 22
SRF Cavity Development-QWR

## Slide 16
SRF Cavity Development-HWR
Frequency (MHz) | Optimum 𝛽 | Eacc (MV/m) | Vacc (MV) | Q0 | # of cavity | # of modules | Op. temp (K)
162.5 | 0.12 | 6.6 | 1.46 | 2.3e+9 | 106 | 35 | 2

## Slide 17
Assembly of the HWR Cryo-module
SRF Cavity Development

## Slide 18
Thermal load of the HWR Cryo-module
SRF Cavity Development

## Slide 19
SRF Linac Assembled and Installed
-Cryomodule(CM) & Warm section is clean assembled in the clean booth@tunnel
-Total Particle counts(size=0.5um above/10 mins) were less than 30 counts
Warm section
CM
CM
CM
SCL3 and Cryo-plant Installation completed 2021 & Beam commissioning just started
SCL3 LINAC installed on 2021

## Slide 20
Plant status
  Mechanical installation and commissioning was done in July, 2022
  Cold box was connected to the Main distribution box.
  First cool down begins September 7, 2022.
Warm compressors
LHe distribution box
Cold box
Plant configuration
  SCL3 cryoplant (4.2 kW @4.5K) for SCL3
  SCL2 cryoplant (13.5 kW @ 4.5 K) for SCL2
  To combine two plants through the distribution box. If one plant down, the other can maintain cold SCL 2&3 together or only one.
Cryo-plants are ready

## Slide 21
Simple Diagram of the SCL3 Cryo-system

## Slide 22
Part 3.
Beam Commissioning Status

## Slide 23
- Injector
* Ion Source: 14.5 GHz ECR IS
* LEBT: 10 keV/u
* RFQ: 507 keV/u, 98% transmission
* MEBT: 507 keV/u, 4 bunchers
- Beams: Ar9+(A/q=4.4), Ar8+(5.0), Ar11+(3.6)
- Beam Diagnostics
14GHz
ECR IS
LEBT
RFQ
MEBT
 | LEBT | MEBT
Allison scanner | 2 (X,Y) | -
Wire scanner | 4 | 4
Faraday cup | 4 | 2
ACCT | 1 | 2
BPM | - | 6
Beam viewer | 2 | 1
Fast Faraday Cup | - | 1
LEBT
28GHz
ECR IS
14GHz
ECR IS
LEBT
RFQ
MEBT
Injector Diagnostics

## Slide 24
Measurements for commissioning
MEBT Bunchers RF set-point (phase scan, BPM)
Beam energy (phase scan, TOF with BPMs)
Beam current, transmission (ACCT, FC)
Orbit correction (BPM / Wirescanner & dipole steerer)
Beam transverse profile (wirescanner)
Transverse matching (wirescanner)
Beam emittance (X and Y) : Allison scanners, Beam size fitting, quad scan methods
Physics applications for commissioning
BIPAM (Beam Input Parameters And Matching)
CAPS (Cavity Amplitude and Phase Scan)
Orbit correction application
Emittance data analysis & wirescanner data analysis
Injector Beam Commissioning

## Slide 25
Beam parameter measurements (Allison scanners, wirescanners)
measuring initial beam parameters (fitting beam sizes of wirescanners)
controlling optics when needed
do matching to RFQ
Emittance measurement (Allison scanner, quad scan)
Beams: Ar9+ (~30A), Ar8+ (~47A)
LEBT beam parameters
Beam emittance
(Allison scanner)
 | X | Y
Allison | 0.048 | 0.067
Quad Scan | 0.041 | 0.038
emittance comparison
Beam emittance
(quad scan)
Low Energy Beam Transport (LEBT)

## Slide 26
- orbit correction
- beam tracking (TRACK, DYNAC codes)
LEBT orbit correction
TRACK (beam dynamics code)
LEBT Orbit Correction

## Slide 27
MEBT beam parameter measurements
using beam sizes from wirescanners
measure initial beam emittances & parameters
can do matching to SCL3
MEBT buncher RF set-point
using phase scan technique
determines RF amplitude & phase
RF set-points of 4 bunchers obtained
Beam energy is 514 keV/u (design 507 keV/u)
ex=0.052
ey=0.059
Medium Energy Beam Transport (MEBT)

## Slide 28
- 10% beam duty operation: 96 minutes, 10Hz, 10msec (2021.12.07.)
* Injector transmission > 94%
- MEBT beam emittance measurement based on quad scan
x = 0.059 mm-mrad
y = 0.081 mm-mrad
Injector beam transmission
MEBT quad scan
emittance measurement
Injector Transmission

## Slide 29
All conditions checked for first cool-down
  - Helium leak tests (final) - done
  - Pressure tightness (final) - done
  - Circulation by SCL3 Cryoplant/check of filters - done
  - Check purity of helium in the cryogenic lines – fine
  - Check insulation vacuum – fine (for starting cool-down)
  - Readiness of all interlock systems - done
  The first cool-down : started @ 7th of Sep. 15:30
Cryo-plants readiness check

## Slide 30
SCL3 Cryogenic Operation Modes (based EPICS + PLC)
Now
Sequences

## Slide 31
Cooling down cryogenic distribution system, thermal shields of all cryomodules with SCL3 cryoplant, simultaneously.
First Cool-down on September 15, 2022
4.5 K reached
End-Box
Control (by-pass flow and stability)
Cavities : Cool-down
Step cool-down (Cryogenic lines, End-box, and all thermal shields)

## Slide 32
Cool-down of Cryomodules
  54 % progress (30 ea/55 ea cooled down)
  All QWR cavities – fast cooled down
  Now, HWR A sections almost finished
Stability
  All cold masses have not been cooled down yet
    Once cooling down all components, need to optimize the stability
  For the first beam commissioning @ QWR CM #1~5
    SHe (Subcooled Helium Supply) – flow rate controlled for stability
    Mitigation by controlling bypass flows (1. GHe return – Very Low Pressure return, 2. End Box) + vibration from flows
    QWR CM #1~6 sections – Control improvement (for Pressure stability by using cryogenic valves + heaters’ control)
First Cool-down Status

## Slide 33
Measurements to perform
QWR/HWR RF set-point (phase scan, BPM)
Beam energy (phase scan, TOF with BPMs)
Beam current, transmission (ACCT, FC)
Orbit correction (BPM & dipole steerer)
Beam transverse profile (wirescanner)
Transverse matching (wirescanner)
Beam emittance (X and Y) : beam size fitting, quad scan
Physics applications for commissioning
BIPAM (Beam Input Parameters And Matching)
CAPS (Cavity Amplitude and Phase Scan)
Orbit correction application
Emittance data analysis & wirescanner data analysis
SRF Linac Commissioning Plan

## Slide 34
Halo Collimators(aperture 36 mm) installed at beam boxes
cryomodule
quadrupole
beam box
Available Diagnostics in QWR Section

## Slide 35
Phase scan with BPMs (Time of Flight measurement)
CAPS (Phase Scan Tool, Cavity RF Setpoint)

## Slide 36
First five QWR modules are activated because of the position of F/C.
Next beam operation aims at delivering beams to HWR A5 (Dec.).
First Acceleration was Done on Oct. 7 !!

## Slide 37
Summary & Outlook
Part 4.

## Slide 38
RAON installation and system integration was successfully done :
Progress rate is more than 97% for Phase 1
Injector beam commissioning was carried out, achieving machine setting and key measurements :
measured beam parameters (energy, emittance, Twiss parameters, beam sizes etc)
capable of controlling LEBT and MEBT beam optics freely as needed
achieved beam transmission of 95% max (routinely > 90%)
machine verification including diagnostics devices
First beam acceleration was demonstrated on Oct. 7 using first five QWR modules :
First cool-down to 4.5K was completed without any serious problems
Next beam commissioning starts after 2K cool-down of HWR modules
Summary & Outlook

## Slide 39
Summary & Outlook
September : Cool-down of QWR/RF conditioning
First Beam injection to first five modules
October : Cool-down of HWR/RF conditioning
November : 2K pumping for HWR section/RF conditioning
December : 2K stabilization for HWR section/RF conditioning
Second beam commissioning toward HWR A5.
January-March : Beam commissioning for whole SCL3
DONE

## Slide 40
Technical Challenges of the Project RISP
Optimize test procedures
Find right cavity treatments
Mature cavity production process
Monitor long transportation
Deal with pandemic issues correctly
Complete long cryo-distribution line without cold leak
Control cryo-plant operation with small thermal load

## Slide 41
Thank You for your attention!