## Slide 1: Low-field Multipacting in FRIB Quarter-Wave Resonators and Its Mitigation
October 11, 2022
TTC2022 at Aomori, Japan
Sang-hoon Kim on behalf of FRIB SRF team

## Slide 2: Outline
Low-field multipacting in FRIB β=0.085 80.5 MHz QWR
Theoretical calculations
Single-stub matching element to improve MP conditioning speed
Experimental results
Discussion
Summary

## Slide 3: Low-field MP in FRIB QWR085
Coaxial MP between inner and outer conductors of QWR
MP band: ~6 kV/m to ~14 kV/m in Eacc (cf. Eacc spec: 5.6 MV/m)
FPC Qext is ‘fixed’ once cryomodule is cooled down: Qext = 2e6
MP electrons at Eacc of 12 kV/m

## Slide 4: Limitation of CW MP Conditioning
Operational and conditioning experience
  Techniques used in FRIB & ReA Linac: pass the MB band during the rising time before MP at “low-field” is built up
  CW MP conditioning in the ReA6 cryomodule (the same as FRIB QWR085 cryomodules): 26 hours at Pfwd of 2 W, 16 hours at Pfwd of ~3 W
ReA6 cryomodule in FRIB ReAccelerator

## Slide 5: Theoretical Explanation
Time-dependent wave propagation model in a resonant cavity system [1]
  Incident wave from the generator Wave ‘reflected from the coupler’ Wave radiated from the cavity Backward wave : Wave ‘reflected from the resonant cavity system’
[1] T. Wangler, “RF Linear Accelerator”, pp. 146 – 148.
: coupling coefficient , : RF filling time, : cavity detuning phase
Chart: Changes in reflected RF power when MP is excited: QWR085, Qext = 2e6, MP @ Ea = 6 kV/m
Power difference = dissipated at multipactor

## Slide 6: Motivation of Stronger Coupling
Chart: Dissipation power at multipactor: QWR085, MP @ Ea = 6 kV/m

## Slide 7: Single-stub Matching Element: Simplified Model
stub position
stub length
single
stub
transmission line
Chart: Qext change with respect to positions and lengths of the single stub
| 0.252 | 0.35199999999999998 | 0.45200000000000001 | 0.55200000000000005 | 0.65200000000000002 | 0.752 | 0.85200000000000009 | 0.95200000000000007 | 1.052
0.1 | 63577300 | 50302400 | 36441000 | 23348000 | 12311300 | 4446570 | 455701 | 751350 | 5303820
0.15 | 26691900 | 20379900 | 14084100 | 8408370 | 3933210 | 1071510 | 107600 | 1133260 | 4050280
0.2 | 14286600 | 10553100 | 6964060 | 3883190 | 1616980 | 377237 | 287699 | 1356390 | 3478380
0.25 | 8812723.7767 | 6311528.6322 | 4004068.4457 | 2121147.3615 | 839400 | 286478.0369 | 514737.2004 | 1503151.1299 | 3153773.6524
0.3 | 5978150 | 4186570 | 2592630 | 1352620 | 586838 | 368897 | 719535 | 1605520 | 2941340
Strongest coupling condition can be obtained when (stub position) + (stub length) ~= λ/4,
FPC is assumed to be lossless in these simulations

## Slide 8: Single-stub Matching Element: Measurements
Regular FPC: Qext = 2.3e6
With single stub: Qext = 1.6e5
(Reduction of Q0 due to normal conducting structure was taken into account)

## Slide 9: Improvement of Conditioning Time with the Single-Stub Matching Element
Chart: Conditioning time with various Qext (8 different cavities in the same cryomodule)
| 2 | 3 | 10 | 20
Qext: 2e6 | 26 | 16 | 6.67 | 6
Qext: 5e5 | 8 | 4
Qext: 1.6e5 | 2.6667 | 1.7333

## Slide 10: Discussion
Applications to linac cryomodules
  Plan for FRIB linac cryomodules
    CW conditioning at a few tens of Watts with the regular FPCs: already completed for ~30% of total 104 QWRs
    For cavities with relatively strong MP: temporarily insert the single-stub matching element for conditioning

## Slide 11: Conclusion
For the low-field MP in FRIB QWRs, theoretical calculations predicted efficient conditioning with higher RF power and/or stronger FPC coupling
Developed a single-stub matching element to externally improve coupling strength. Experimental results on MP conditioning time are consistent with theoretical predictions
More statistical results will be obtained as we perform conditioning of FRIB Driver Linac QWRs