## Slide 1: TTC WG4 Summary
Rongli Geng, Camille Ginsburg, Francesco Grespan, Michiru Nishiwaki

## Slide 2: SPC Charges to WG4
WG-4: Availability and operability of existing accelerators compared to their design goal
Many SRF accelerators for electron, proton and heavy ions have been under long term beam operation (more than 5 years). In addition to the cavity quality factors and gradients, the availability and operability of the SRF accelerator are key metrics for performance.
The WG-4 scope includes presentations and discussions on the experience gained operating existing SRF accelerator facilities including long term cavity performance, key sources of down-time and key sources of procedural time. Discussions would include issues such as field emission, multipacting, trapped flux, cryogenic and rf issues and issues with cavity ancillaries. Also of interest are the development of mitigations designed to reduce down-time and improve operability including maintenance planning, high level applications and on-line processing. The causes of the performance limitations and the trip rate during beam operation should be presented.
10 contributions in 2 sessions
6 contributions in 2 sessions
Touched upon but more needed

## Slide 3: Machine Availability (A) and Reliability (R)
Electron machines
  CEBAF at JLab (McCaughan)
  LCLS-II at SLAC (Aderhold) – beam operation to be started
  PLS-II at PAL (Sohn)
  cERL at KEK (Sakai)
  SuperKEKB at KEK (Nishiwaki)
  EuXFEL/FLASH at DESY (Reschke)
Proton/Heavy ion machines
  SRILAC at RIKEN (Yamada) – 3 years beam operation
  FRIB at MSU (Kim) – 6 months beam operation
  SNS at ORNL (Geng)
  ISAC-II at TRIUMF (Yao)
15 min allotted each speaker
5 min presentation 3 slides
10 min discussion
Common questions (next slide)
Regional breakdown
50% North America
40% Asia
10% Europe
5+ years beam operation

## Slide 4: Common questions
How is the availability defined? Is there a requirement for the availability?
What are the top 3 SRF failure modes?

## Slide 5: Improving cavity/cryomodule performance
Plasma processing at JLab (Ruber)
Plasma processing at FNAL (Belomestnykh)
ESS medium beta cavity recovery (Monaco)
SRF/RF recovery in CEBAF at JLab (McCaughan)
Operating experience in ISAC-II Linac at TRIUMF (Yao)
Horizontal HPR in SuperKEKB at KEK (Okada)
30 min allotted each speaker
Regional breakdown
67% North America
17% Asia
17% Europe

## Slide 6: Main Takeaway Messages
High availability (HA), >98%, operation of SRF accelerators demonstrated
  Large (tens to hundreds of SRF cavities) or small (a few SRF cavities)
  Circular or linear
  Electron or hadron
HA always desired but usually not “required”
  “discovery” accelerator may push energy reach at cost of lower availability
  “production” accelerator may seek balance between operation hours and A

## Slide 7: Common Themes
For electron machines, a monolithic cold string appears to reduce degradation
  No data for hadron/heavy ion machines
  Warm sections, especially moving instrumentation like wire scanners, are a potential source of particulates which is a risk if particulates migrate to neighboring cryomodules
All labs have established performance monitoring and possible recovery
Redundancy is important
Preventing SRF beamline leak or air inrush is important for its high impact
Need for mitigating field emission in operational SRF cavities is driving creative solutions

## Slide 8: Differences
Sources of major downtime vary among labs
  Example: for CEBAF, the linacs are the largest single area of downtime; for EuXFEL, the linacs are among the smallest
No common definition of or requirement for machine availability
  Example: XFELs have to compete in the light source scientific user community with storage rings which provide uptimes of >99%
  DOE
Wide range of scheduled hours per year impacts uptime requirements
Impact of short vs long runs

## Slide 9: Cavity Recovery
Each facility has is own unique approach.
It is important to have countermeasures for both of minor (e.g. gradient loss in time) and fatal degradations to keep the quality of the accelerator.
  In CEBAF, Plasma processing for FE and radiation.
  In SuperKEKB, Horizontal HPR for particulate contamination.
Another important thing is to minimize unexpected degradation.
  Need reliable interlock and hardware system.
Cavities never die – they can be recovered any number of times.

## Slide 10: Looking Ahead
A good start on the topic
HA&R anticipated to become a requirement for future SRF accelerators
  ADS (due to physical reason arising from beam target interactions)
  Commercial and medical applications (for customer satisfaction and patient safety)
Failure modes and root cause studies including fault propagation crucial
  For maturing SRF accelerators to achieve HA
  For matured SRF accelerators to sustain HA
TTC the perfect platform to drive this topic for discussion & exchange
Thanks to all speakers for their high-quality presentations which made WG4 sessions productive and stimulating